## Slide 1
teuscher@pdx.edu
www.teuscher-lab.com
Portland State University
Department of Electrical and Computer Engineering (ECE)
Emerging devices and technologies
Christof Teuscher
ECE 410/510: Hardware for AI and ML

## Slide 2
Unconventional computing
Technology Brief | Taking Neuromorphic Computing to the Next Level with Loihi 2
Unconventional Computing
?

## Slide 3
Neuromorphic chips are specialized hardware designed to mimic the structure and function of the human brain. Unlike traditional computing architectures, these chips are built to process information in ways similar to biological neural networks.
What are neuromorphic chips?
Cerebras WSE-3
300-millimeter wafer
4 trillion transistors
TSMC 5nm
57x larger than an NVIDIA H100
Accelerate AI workloads, particularly training and inference of large language models.
Not considered a neuromorphic chip

## Slide 4
The usual trade-offs…!
Flexibility
Performance
IBM’s TrueNorth
IBM’s NorthPole
SpiNNaker
Akida
Loihi
Loihi/2
BrainScaleS/2
T1
Other trade-offs:
Power
Reliability
Programmability
On-chip learning
Cost
Scalability
More analog circuits
But:
Digital backend needed
DAC/ADC
More digital circuits
Why not do everything in software?
DOI: 10.1109/TCSI.2010.2089556
LIF neuron

## Slide 5
https://doi.org/10.3389/fnins.2022.959626

## Slide 7
Loihi 2
DOI 10.1109/SiPS52927.2021.00053

## Slide 8
LLM on Loihi 2
arXiv:2503.18002v2
Why is that gain performance not impressive?

## Slide 9
Akida
Akida (Vanarse et al., 2019) is the first commercial neuromorphic processor, commercially available since August 2021.
BrainChip's Akida is an ultra-low-power neuromorphic processor inspired by the brain’s neural architecture. It accelerates complex AI at the edge through event-based processing, on-chip learning abilities, and support form advanced neural networks like CNNs, RNNs & custom Temporal Event-based Nets.
Temporal Event-based Neural Networks (TENNs), which combine spatial and temporal convolutions to efficiently process sequential spatiotemporal data.
Akida’s ecosystem provides a free chip emulator, TensorFlow compatible framework MetaTF for the transformation of convolutional and fully connected neural networks into SNN, and a set of pre-trained models.

## Slide 10
Do we need brain-like HW?
DOI: 10.3389/fnins.2024.1465789
“Although efforts to address neuromorphic solutions through hardware based on top-down CMOS-based technologies have obtained interesting results in terms of energetic efficiency improvement, the replication of brain’s self-assembled and redundant architectures
is not considered in the roadmaps of data processing electronics.”

## Slide 11
https://doi.org/10.1038/s41467-025-57352-1

## Slide 12
https://doi.org/10.1038/s41586-024-08253-8

## Slide 13
https://doi.org/10.1038/s41586-024-08253-8
Progression of neuromorphic computing systems

## Slide 14
https://doi.org/10.1038/s41586-024-08253-8
Feature maturation of neuromorphic computing

## Slide 15
https://doi.org/10.1038/s41586-024-08253-8
Gaps in neuromorphic computing

## Slide 16
Are spikes the future for LLMs?
SNN can’t be trained with backpropagation. STDP is used instead.
  Local learning only
  Credit assignment problem
  Lack of scalability and efficiency
  Lack of global optimization objective
  No mathematical convergence guarantee
Transformers are inherently un-brain–like.
The attention mechanism requires matrix-matrix multiplication. Hard to implement in neuromorphic architectures.

## Slide 17
Recap: neuromorphic chip design choices
Spikes vs analog
Stochastic vs reduced precision vs full precision
In-memory vs near-memory vs von Neumann
NoC vs shared bus vs wires
Inference and/or learning
Crossbar vs non-crossbar
Neuron circuitry vs configurable neuron vs programmable neuron
STDP vs backprop vs other learning rules
Embedded vs datacenter
Number of neurons vs complexity of neuron and/or learning rate
Amount of memory

## Slide 18
What other options do we have to
accelerate AI/ML algorithms?

## Slide 19
Mem-elements
Compute closer to the physics.
Compute with the physics.

## Slide 20
Mem-elements
1971: Chua predicted missing circuit elements
https://doi.org/10.1038/nature06932
Memristor:
Variable resistance that depends on the history of current that has flowed through the device.
Ability to "remember" its previous resistance state even when power is turned off.
Non-volatile memory properties (retains information without power)
HP: TiO₂ devices

## Slide 21
Memristors
https://doi.org/10.1038/nature06932

## Slide 22
Memcapacitor and meminductor
DOI: 10.1109/TCSII.2014.2387653
Memristor state change: apply an electric current through the device.
Memcapacitors store energy in electric fields and respond to voltage history rather than current history.
Meminductor state change: create magnetic flux.

## Slide 23
Memristors for neuromorphic chips
DOI: 10.1109/TNNLS.2013.2296777
What to do with negative weights?
Positive weights
Negative weights

## Slide 24
Memristors can implement STDP
https://doi.org/10.1038/s41467-018-07757-y
STDP emerges naturally from device physics without complex circuits.
STDP: The time difference between spikes determines magnitude of change (closer timing = stronger effect)
STDP refines Hebbian learning by adding precise timing relationships. Unsupervised learning!
Memristors typically have threshold voltages required for changing state.
Only when spikes overlap sufficiently does voltage exceed the threshold.

## Slide 25
VMM using memristive crossbars
DOI: 10.1109/NANOARCH.2017.8053729

## Slide 26
What is one problem of memristors?
https://www.nature.com/articles/s41928-021-00649-y

## Slide 27
Memcapacitors
https://doi.org/10.1038/s41928-021-00649-y
Memcapacitors offer several unique benefits, but one of their most significant advantages is their exceptional energy efficiency in dynamic computing applications.
Memcapacitors can implement STDP too (through charge).

## Slide 28
Issues with mem-devices
https://doi.org/10.1038/s41928-021-00649-y
Device-to-device variation
Cycle-to-cycle variation
Limited write cycles (106-109 compared to CMOS >1015)
Retention issues / state drift
Programming complexity (requires precise pulses)
Limited switching speeds
Lack of design tools

## Slide 29
Unconventional computing
Technology Brief | Taking Neuromorphic Computing to the Next Level with Loihi 2
Unconventional Computing
?

## Slide 30: What is computation?
Computation
Mapping
Transformation
Function Ot+1=f(It)
Inputs I
Outputs O
…
…
How can we “realize” this mapping?

## Slide 31: Intrinsic vs designed computation
Device network
Computing architecture
Intrinsic dynamics
Desired computation
How to obtain a desired computation?

## Slide 32: What is Unconventional Computing (UCOMP)?
“[…] a computing scheme that today viewed as unconventional may well be so because its time hasn’t come yet – or is already gone.” — Tommaso Toffoli
"Today, UCOMP is broad but (relatively) shallow, whilst CCOMP is narrow, but incredibly deep. What would computation look like if UCOMP were as deep as CCOMP, and there were an integrated theory combining all its aspects?" — Susan Stepney
There is no precise definition…

## Slide 33: Today’s unconventional computing spectrum (1)
Mem-element computing
Hypercomputation
Quantum computing
Ising machines
Analog computing
Reservoir computing
More classical
More unconventional
In-memory computing
Multi-core
GPU
Neuromorphic
DNA computing
Thermodynamic computing
Cellular automata
Membrane computing
Stochastic computing
FPGA
Bacterial computation
Chaos computing
What should I “invest” in to reboot computing?
Fluidics
Most definitely incomplete…
Materials – Devices & Circuits – Architectures – Software – Algorithms – Applications
”Fringe”

## Slide 34: Today’s unconventional computing topics spectrum (2)

## Slide 35: The unconventional computing spectrum over time
More classical
More unconventional
”Fringe”
Time
Examples:
FPGAs
reservoir computing
Neuromorphic computing

## Slide 36: The unconventional computing time horizon
Industry
Today
5 years
10 years
15 years
20 years
More un- conventional
Unconventional
…

## Slide 37: Hype or computation?
Gartner’s hype cycle
FPGAs
GPUs
DNA computing
Quantum computing
Thermodynamic computation

## Slide 38: UCOMP supporters
UCOMP critics
👍🏻
👎🏻
No useful paradigms that can compete with conventional approaches.
The real, practical challenges to be solved are always kept comfortably far away.
Proving that we can compute a NAND function with a self-assembled nanowire network, for example, doesn’t move the needle.
New technologies need time (and money) to mature.
Current comparison with state-of-the-art are not fair comparisons.
We need to start somewhere.
Often on shoestring budgets only.

## Slide 39: Evolution of the popularity of “unconventional computing”
Source: Engineering Village, Inspec
Several conferences and journals
Time

## Slide 40: The decline of traditional computer architecture
The number of records over the years that were found for the “computer architecture” thesaurus term. The field had its peak around 1985 and has since been in decline. Data source: Elsevier Engineering Village thesaurus.

## Slide 41: Popularity of selected individual UCOMP approaches
Source: Engineering Village, Inspec
Stochastic
Thermodynamic
Hypercomputation
Reservoir

## Slide 42
Source: Engineering Village, Inspec
Cellular automata
Reservoir computing
Hit?
Miss?
What did we overlook?

## Slide 43: What is material and Physical Reservoir Computing (PRC)?
A physical reservoir computer is a system in which the reservoir is realized with a physical system.
Source: Tanaka et al., Recent advances in physical reservoir computing: A review, 2019, https://doi.org/10.1016/j.neunet.2019.03.005

## Slide 44: Questions of interest for Physical Reservoir Computing (PRC)
How much control does on have over the fabrication process?
Reproducibility of input-output mapping?
How to interface with a material/device?
Memory capacity?
Signal attenuation/amplification?
Cycle-to-cycle variation?
Device-to-device variation?
In-situ or ex-situ training? The challenging part tends to be the in materio implementation of the readout and training.
What pre- and post-processing is necessary? What will it “cost?”
…

## Slide 45: Pattern recognition in a bucket (1)
DOI: 10.1007/978-3-540-39432-7_63
Water tank
Overhead projector
4 electric motors perturb water surface
320x240 pixels, 5 frames webcam films inference patters
Sobel edge detection mask that was suitably thresholded to remove noise and averaged to produce a 32x24 grid. The cells of this matrix were used as the input values for 50 perceptrons in parallel
XOR task
Speech recognition (“zero”/”one” task)
  25% mistakes with single perceptron
  1.5% mistakes when passed through water.

## Slide 46: Pattern recognition in a bucket (2)
Fernando and Sajakka experiment replication.

## Slide 47
RC based on solitary-like waves dynamics of film flows
Maksymov & Pototsky, Reservoir computing based on solitary-like waves dynamics of film flows: a proof of concept, 2023, https://arxiv.org/abs/2303.01801
Mackey-Glass time series task
An electric signal modulates the pump flow: ’1’ states are implemented as a brief change in the flow rate that results in the generation of one.
Camera used for outputs. Output layer in software.

## Slide 48: Plant reservoir computing

## Slide 49
Coulombe, Computing with networks of nonlinear mechanical oscillators, 2017, https://doi.org/10.1371/journal.pone.0178663
Computing with networks of nonlinear mechanical oscillators
Anharmonic = not simply harmonic
Springs with damping. Random couplings.
N= 400 oscillators
Parity + spoken words tasks
Numerical simulations only.
Training
Target
Network output
Parity task
Different parities
u(t)

## Slide 50: Reservoirs with atomic switch networks
Lilak, Woods, Scharnhorst K, Dunham, Teuscher, Stieg, Gimzewski, Spoken Digit Classification by In-Materio Reservoir Computing With Neuromorphic Atomic Switch Networks, 2021, http://doi.org10.3389/fnano.2021.675792
Silver iodide (Agl) junctions
Spoken digits task
Self-organizing systems
14 electrodes

## Slide 51: Dynamic memristors for temporal information processing
Source: Du et al. Reservoir computing using dynamic memristors for temporal information processing. Nat Commun 8, 2204 (2017). https://doi.org/10.1038/s41467-017-02337-y
Experimental demonstration of a memristor-based RC system using dynamic
memristor devices that offer internal, short-term memory effects. 88 memristors.
State decay
Implemented in Matlab

## Slide 52: Reconfigurable perovskite nickelate electronics
Source: Zhang et al., Reconfigurable perovskite nickelate electronics for artificial intelligence, 2022, https://doi.org/10.1126/science.abj7943
Perovskite nickelate devices act as memristors and memcapacitors for RC.

## Slide 53: First Josephson Junction (JJ) reservoir (1)
Rowlands et al., Reservoir Computing with Superconducting Electronics, 2021, https://arxiv.org/abs/2103.02522
Josephson transmission line (superconducting oscillators)
>100GHz
Inputs to selected JJs only
Wave-like reservoir response
https://www.youtube.com/watch?v=1bWjyQ1326g
Toggle FF
Task: speech recognition. ~70% accuracy. 5 JJs.
Signal reconstruction

## Slide 54: First Josephson junction reservoir (2)
Article: Rowlands et al., Reservoir Computing with Superconducting Electronics, 2021, https://arxiv.org/abs/2103.02522
Screenshots from https://www.youtube.com/watch?v=1bWjyQ1326g
Actual JJ chip

## Slide 55
Paquot et al., 2012, http://www.doi.org/10.1038/srep00287
Optoelectronic RC (general idea)
Photonic reservoirs are all about high speed. The challenge is to make them small.
Non-linearity
Previous state
Input
New state
Input
Mach-Zehnder modulator

## Slide 56
Goudarzi, Lakin, and Stefanovic, DNA reservoir computing: a novel molecular computing approach, 2013, https://doi.org/10.1007/978-3-319-01928-4_6
DNA oscillators as reservoirs
Readout in software
Microfluidic reaction chamber
Input species
Yahiro et al., Alife, 2018, https://doi.org/10.1162/isal_a_00013
Used same oscillator as Goudarzi et al.
Simulation only. Similar performance as Goudarzi.
Cycle
Line

## Slide 57: Open problems, challenges, and opportunities
Scale up PRC systems to massive numbers of neurons.
Train modular/hierarchical reservoirs efficiently.
Multitasking reservoirs.
Lifelong/incremental learning with growing reservoirs (developmental systems).
Implement readout/learning directly in materio.
Find sweet spots for high-speed, low-power, high performance, and high robustness.
Reservoirs that adapt, are tuned, or reconfigured (in-situ).
Material reservoir (deep) co-evolution.

## Slide 58: Quo vadis?
Material computing has attracted increasing attention: it allows for solving computational problems for which traditional, general-purpose architectures are not efficient.
PRC has great potential for physically “embedding” computing in a substrate by using the substrate itself to perform the computation.
A broad(er) success of PRC will be contingent on finding solutions to the open questions and challenges: identify physical substrates, scaling up hardware, scaling up programmability → (deep) co-design.

## Slide 59: What are good metrics to evaluate UCOMP approaches?
Gain
Signal to noise ratio
Scalability
“[...] there is nothing on the horizon that has promise to replace CMOS at least in the next ten to fifteen years.”
IRDS 2022, BC
Is that still true?

## Slide 60: The goals and drivers have changed and keep changing
Avogadro-scale computing
Large number
IDRD, 2022, BC

## Slide 61: Deep co-design: our best path forward?
Given a proposed unconventional computing substrate, we can ask:
Does it actually compute?
If so, how well does it compute?
Can it be made to compute better?
Given a proposed unconventional computational model, we can ask:
How powerful is the model?
Can it be implemented in a substrate?
How faithfully or efficiently can it be implemented?
Given complete freedom in the choice of model and substrate, we can ask:
Can we co-design a model and substrate to work well together?
Stepney, S., Co-designing the computational model and the computing substrate. In Proceedings of the 18th International Unconventional Computation and Natural Computation Conference, pp 5-14, 2019.

## Slide 62: Deep co-design across the entire stack

## Slide 63: Deep co-design: what we need to make this happen…
A formal framework for in-materio computing:
  continuous
  open
  stochastic
  non-equilibrium
  non-linear
  …
Revisit the stack (or get rid of it?)
More comprehensive design space exploration at all levels.
Stepney, 2018

## Slide 64
Each paradigm has unique strengths and faces distinct challenges. The most practical near-term applications are likely in specialized neuromorphic chips while quantum and DNA computing represent longer-term possibilities for specific problem domains.
The reality is that future computing systems will likely be hybrid, combining multiple paradigms to leverage their respective strengths - such as using photonic interconnects with electronic processors, or quantum-classical hybrid systems for optimization problems.

## Slide 65: Where should we look for the next big thing?
ICRC 2023
poll

## Slide 66: Look for specialists, not generalists

## Slide 67: Action items for the community
Look for specialists
Formal frameworks
(Unified?) evaluation metrics
Roadmap(s)
Timelines to solutions
Scott Holmes