## Slide 1
teuscher@pdx.edu
www.teuscher-lab.com
Portland State University
Department of Electrical and Computer Engineering (ECE)
Hardware for AI and ML Overview + Co-design
Christof Teuscher
ECE 410/510: Hardware for AI and ML

## Slide 2
What is a computer?
What’s the job of a computer architect / chip designer?

## Slide 3: What is computation? (1)
Computation
Mapping
Transformation
Function Ot+1=f(It)
Inputs I
Outputs O
…
…
How can we “realize” this mapping?

## Slide 4: What is computation? (2)
Inputs I
Outputs O
…
…
Look-up table
Simple, fast
I1 | … | IN | O1 | … | OM
0 | … | 1 | 1 | … | 0
1 | … | 0 | 0 | … | 0
… |  |  |  |  | 

## Slide 5: What is computation? (3)
Inputs I
Outputs O
…
…
Neural network
Universal function approximator
…
(Hornik, Stinchcombe, White, 1989, https://doi.org/10.1016/0893-6080(89)90020-8)
Feedforward
No memory/state
Generalization
Input nodes
Hidden nodes
Output nodes
Weights
Various training algorithms
Guaranteed convergence

## Slide 6: What is computation? (4)
Inputs I
Outputs O
…
…
Memory is needed in a lot of cases
Temporal signal processing (audio, video)
Timeseries prediction
Control tasks
Feedback
Dynamical system

## Slide 7: What is computation? (5)
Inputs I
Outputs O
…
…
Recurrent neural networks (RNN)
Training is challenging, various algorithms exist (backpropagation through time), convergence not
guaranteed, many weights, slow learning. RNNs are also universal function approximators
(Schaefer & Zimmerman, 2007, https://doi.org/10.1142/S0129065707001111)
…
…
Hidden nodes
Output nodes
Weights
Input nodes
Recurrent connections
Dynamical system
Integration over time

## Slide 8: What is computation? (6)
Inputs I
Outputs O
…
…
…

## Slide 9: Intrinsic vs designed computation (2)
Device network
Computing architecture
Intrinsic dynamics
Desired computation
How to obtain a desired computation?

## Slide 10: Intrinsic vs designed computation (3)
Kron, Gabriel. "Electric circuit models of partial differential equations." Electrical Engineering 67, no. 7 (1948): 672-684.
vs

## Slide 11: Intrinsic vs designed computation (4)
vs
https://www.analog.com/en/resources/design-notes/using-a-generic-0-to-1v-analog-multiplier-to-ensure-accurate-power-management.html

## Slide 12: What are the design trade-offs?

## Slide 13: What are the design trade-offs?
Performance
Flexibility (general purpose vs application-specific)
Energy efficiency
Power density (avoid burning chip, cost of cooling technology)
Design complexity
Design cost
Scalability
Shrinking design schedules (time-to-market)

## Slide 14: What is (HW/SW) co-design?
The practice of taking the best from software design and the best from hardware design to solve design problems.
HW/SW co-design deals with HW/SW interfaces.
HW/SW co-design is the design of cooperating HW and SW components in a single design effort.
Why design new HW if there is already one available to do the job? E.g., a RISC processor?
From a flexibility and design effort perspective, as much as possible should be in software. [Easy, flexible, available libraries, etc.]
Schaumont, 2013

## Slide 15: Why is HW/SW co-design important for AI/ML
Performance optimization: Traditional hardware design assumes fixed software, while traditional software design assumes fixed hardware. Co-design breaks this barrier by simultaneously optimizing both, leading to significant performance improvements for AI workloads.
Specialized acceleration: AI algorithms have unique computation patterns (like matrix multiplications and convolutions) that benefit from custom hardware accelerators tailored to these specific operations.
Memory bottlenecks: AI models face severe memory bandwidth constraints. Co-designing hardware memory hierarchies with software that efficiently schedules operations can minimize data movement and maximize throughput.
Energy efficiency: By tailoring hardware precisely to the needs of ML workloads and optimizing software to take advantage of hardware capabilities, co-design dramatically reduces power consumption, which is critical for both data centers and edge devices.

## Slide 16: Cryptography on small embedded platforms
Schaumont, 2013
What do we learn here?

## Slide 17: Cryptography on small embedded platforms
Schaumont, 2013
Hardware crypto-architectures have, on the average, a higher relative performance compared to embedded processors.

## Slide 18: Cryptography on small embedded platforms
Schaumont, 2013
AES for different target platforms
What do we learn here?

## Slide 19: Driving factors in HW/SW co-design + dualism
Schaumont, 2013

## Slide 20: The HW/SW co-design space
Schaumont, 2013
ASIP = Application Specific Instruction Processor

## Slide 21: The goals and drivers have changed
Avogadro-scale computing
Large number
The number of units in one mole of any substance is called Avogadro's number or Avogadro's constant.
6.02×1023
CM 1 & 2: Up to 65,536 1-bit processors

## Slide 22: The goals and drivers have changed
https://royalsocietypublishing.org/doi/10.1098/rsta.2019.0061

## Slide 23: Deep co-design across the entire stack

## Slide 24
Paper discussion
What did you learn?

## Slide 25
Paper discussion (1)
The difference between these papers shows how the field of co-design has evolved from general principles to specialized approaches for complex AI systems over nearly three decades.
LLMs face unique challenges compared to traditional deep learning systems, requiring extensive computational resources, high energy consumption, and complex software optimizations.
LLMs differ from CNNs in their memory requirements and processing patterns, requiring unique co-design methodologies.

## Slide 26
Paper discussion (2)
Co-design is about a systems perspective: meeting system-level objectives.
Co-design is the key to designing efficient systems.
Designing HW is increasingly like designing SW.
Flexibility vs performance trade-off.
  E.g., reconfigurability increases usability, but does not increase performance.
Co-design tools: modeling, validation, implementation.
Identify critical segments of SW and run them on special HW.
LLMs require unique optimization strategies.
  GPT-3: 175 billion parameters, 350GB of GPU memory just for parameters
GPUs are the cornerstone of modern deep learning infrastructure.

## Slide 27
Paper discussion (3)
Guo et al., 2025

## Slide 28
What is Artificial Intelligence (AI)?
What is Machine Learning (ML)?

## Slide 29
AI vs ML
Machine Learning (ML) is one technique used to achieve Artificial Intelligence (AI).
All ML is AI, but not all AI is ML.
AI is the destination (e.g., intelligent machines), while ML is one path to get there (learning from data).
Artificial Intelligence (AI): Broader concept encompassing machines that can perform tasks requiring human intelligence. Ultimate goal: Artificial General Intelligence (AGI)
Machine Learning (ML): Subset of AI focused specifically on algorithms that improve through experience. Example: neural networks

## Slide 30
AI vs ML
Source: Tignis

## Slide 31
A very brief history of AI
Strong AI = AGI = Artificial General Intelligence

## Slide 32
https://medium.com/@lmpo/a-brief-history-of-ai-with-deep-learning-26f7948bc87b
A very brief history of AI with deep learning

## Slide 33
An abstract neuron
Rojas, 1986

## Slide 34
A neural network
Rojas, 1986

## Slide 35
Special types of neural networks
Rojas, 1986

## Slide 36: Types of neural networks
(Fjodor van Veen, 2016, asimovinstitute.org)

## Slide 37
Deep neural networks

## Slide 38
Transformers are deep neural networks
https://builtin.com/artificial-intelligence/transformer-neural-network

## Slide 39
Learning
Mishra et al., 2023
What is harder? Inference or training?

## Slide 40
Mishra, Ashutosh; Cha, Jaekwang; Park, Hyunbin; Kim, Shiho. Artificial Intelligence and Hardware Accelerators, 2025

## Slide 41
Source: “Bridging Biological and Artificial Neural Networks with Emerging Neuromorphic Devices: Fundamentals, Progress, and Challenges”
There are two general approaches to developing artificial general intelligence (AGI):
computer-science-oriented and
neuroscience-oriented

## Slide 42
Neuromorphic Computing with Large
Scale Spiking Neural Networks

## Slide 43
AlexNet: A classical deep convolutional neural network
Liu & Law, Artificial Intelligence Hardware Design, 2021
AlexNet paper: https://papers.nips.cc/paper_files/paper/2012/file/c399862d3b9d6b76c8436e924a68c45b-Paper.pdf

## Slide 44
Deep learning HW issues
Liu & Law, Artificial Intelligence Hardware Design, 2021
FC = fully connected

## Slide 45
Exploiting parallelism
Does that come at a cost?

## Slide 46
Hardware for AI/ML

## Slide 47
General co-processing mechanism
Mishra, Ashutosh; Cha, Jaekwang; Park, Hyunbin; Kim, Shiho. Artificial Intelligence and Hardware Accelerators, 2025

## Slide 48
General AI accelerator architecture
Mishra, Ashutosh; Cha, Jaekwang; Park, Hyunbin; Kim, Shiho. Artificial Intelligence and Hardware Accelerators, 2025
GEMM = General Matrix Multiply

## Slide 49
Hardware for AI/ML
Mishra et al., 2023
Metrics

## Slide 50
Hardware for AI/ML
Mishra et al., 2023

## Slide 51
Hardware for AI/ML
Mishra et al., 2023

## Slide 52
Hardware for AI/ML
Mishra et al., 2023

## Slide 53
Architecture of a TPU accelerator
Mishra et al., 2023
The main component of TPU is the MXU that consists of 256 by 256 (i.e., 65,536) MACs to perform 8-bit mathematical operations.
The MXU gets its input from the weighted FIFO and unified buffer (UB).

## Slide 54
Hardware for AI/ML
Mishra et al., 2023

## Slide 55
General AI accelerator architectures of FPGA and ASIC
Mishra, Ashutosh; Cha, Jaekwang; Park, Hyunbin; Kim, Shiho. Artificial Intelligence and Hardware Accelerators, 2025

## Slide 56
Deep learning frameworks
Deep learning frameworks provide interfaces to implement AI functionalities regardless of hardware or computing platforms.
Most deep learning frameworks also optimize the network in a hardware-friendly manner and utilize the hardware resources and acceleration functions as much as possible.
Because GPUs are commonly used in deep learning, deep learning frameworks widely support constructing and deploying neural networks on GPU and actively reflect the acceleration support from GPU vendors.
In addition, they provide optimizations on standalone accelerators such as TPU and specific environments such as cloud servers.
Mishra, Ashutosh; Cha, Jaekwang; Park, Hyunbin; Kim, Shiho. Artificial Intelligence and Hardware Accelerators, 2025

## Slide 57
Food for thought
Why is executing a neural network on a general purpose computer inefficient?
What circuitry/processor would you design to find the shortest path in large graphs?
  What if the graph is dense?
  What if the graph is sparse?
What circuitry/processor would you design to recognize QR codes for an embedded camera?
  Recognition needs to be fast and low-power.